Design of a Differential Drive Robot

A differential wheeled robot is a mobile robot whose movement is based on two separately driven wheels placed on either side of the robot body. It can thus change its direction by varying the relative rate of rotation of its wheels and hence does not require an additional steering motion.

Motor Selection

 The Motors (DC) are selected after looking into their parameters. Some of the important parameters are

- Input voltage,current.
- Torque rating
- RPM

Caluclation of RPM :

Let the,

Speed of the robot	= V m/s
Diameter of the wheel = D m

Then the RPM is determined by the equation

RPM = ((60 * Speed /(3.14 * Diameter of Wheel))	(1)

Calculation of Motor Torque :

Let the ,

Number of wheels = Nw
Number of motors =Nm
Radius of Wheels = r (meters)
Total weight of the Robot = M kg

The weight acting on each wheel is N = M/Nw (2)

Assume that the robot is stationary. The maximum torque is required when the robot starts moving. It should also overcome friction.

We can write the frictional force as robot torque = 0 until the robot moves. If we get the robot torque in this condition, we get the maximum torque
as follows:

μ * N * r - T = 0 (3)
where μ is the coefficient of friction, N is the average weight acting on each wheel (according to equation 1) , r is the radius of wheels, and T is the torque.

T (Nm) = μ * N * r	(4)

Example :

1) To Design a Differential drive system , which has a speed of 0.5 m/s and has a weight of 200Kg.

Let the radius of the wheel be = 20cm

Caluclation of RPM :

According to equation (3) the RPM is determined as

RPM = ((60 * Speed /(3.14 * Diameter of Wheel))

= ((60 * 0.5 / (3.14*20*10-2))

= 47.77 Rpm

a motor of approximately 50RPM can be used.

Calculation of Motor Torque :

- Number of Wheels = 4
- N = M/Nw = 200/4 = 50 kg/wheel
- Assume that the robot is stationary. The maximum torque is required when the robot starts moving. It should also overcome friction.
- T (Nm) = μ * N * r
- Let μ = 0.7 (coefficients of friction of dry road)

= 0.7*50*5*10-2
= 1.75 Nm
= (1.75 *100 / 9.8) = 17.85 kg-cm

The design summary
After design, we calculated the following values:

- Motor RPM = 50
- Motor Torque = > 17.85 kg-cm
- Wheel Diameter = 5cm