Differential Steering System and Robot Kinematics

Robot kinematics is the study of the mathematics of motion without considering the forces that affect motion. It mainly deals with the geometric relationships that govern the system.
A mobile robot or vehicle has six degrees of freedom (DOF) expressed by the pose (x, y, z, roll, pitch, and yaw). It consists of position (x, y, z) and attitude (roll, pitch, and yaw). Roll refers to sidewise rotation, pitch refers to forward and backward rotation, and yaw (called the heading or orientation) refers to the direction in which the robot moves in the x-y plane. The differential-drive robot moves from x-y in the plane, so the 2D pose consists mainly of x, y, and θ, where θ is the head of the robot that points in the forward direction of the robot. This much information is sufficient to describe a differential robot pose.

The pose of the robot in x, y, and θ in the global coordinate system

Forward Kinematics :
The forward kinematics equation can be derived as follows. Consider a single wheel of the robot.

When the robot is about to perform a rolling motion, the robot must rotate around a point that lies along its common left and right wheel axes. The point that the robot rotates around is known as ICC- Instantaneous Center of Curvature (ICC). The following diagram shows the wheel configuration of differential-drive with ICC:

 v = 2 πr / T, where T is the time taken to complete one full turn around ICC. The ω angular velocity is defined as 2 π / T and typically has the unit radians (or degrees) per second. Combining the equations for v and w yields ω= 2 π / T.

v r = ω (1)
Now let us fix the coordinate system and derive the further equations

Applying Equation (1) to the above diagram we obtain
Vl = (R - l/2)*ω (2)
Vr = (R+l/2)*ω (3)
 R is the distance between ICC and the midpoint of the wheel axis and l is the length of the wheel axis.
Solving equation (2) and (3) for R and ω we obtain:
Vl - Vr = l*ω
Vl + Vr = 2*R*ω
this implies
ω = (Vr - Vl)/l	(4)
R = (Vl + Vr )/ (2*ω)
R = (l*(Vl + Vr ))/(2*(Vr - Vl))	(5)

Suppose the robot moves with an angular velocity of ω for δt seconds, it can change the robot's orientation
        θ1 = ωδt+ θ
The ICC of rotation is Given by the equations

Given a starting position (x, y), the new position (x', y') can be computed using the 2D rotation matrix. The rotation around ICC with angular velocity ω for δt seconds yields the following position at t + δt time:

ω can be computed Vr and Vl are often difficult to measure accurately. Instead of measuring the velocity, the rotation of each wheel can be measured using a sensor called wheel encoders. The data from the wheel encoders is the robot's odometry values. These sensors are mounted on the wheel axes and deliver binary signals for each step the wheel rotates (each step may be in the order of 0.1 mm). These signals are fed to a counter such that vδt is the distance travelled from time t to t + δt. We can write:

where,